## Slide 1: ROS practice: Mapping and Follow me!
ERNI Embedded Community - November 2018
Jordi Rebull

## Slide 2
Swiss Software Engineering: betterask.erni

## Slide 3: Bridging the gap from simple to complex robotics

## Slide 4: Challenges in robotics:
World is asynchronous. Sequential programming is not suitable.
Robots are complex systems.
Wide diversity of robots, sensors, programming languages, etc.

## Slide 5: Summary
ROBOTICS NEED:
  Callbacks
  Separated processes that communicate through a messaging interface.
  Hardware abstraction
There is a software infrastructure that enables this (among many other things) and it is called:
Swiss Software Engineering: betterask.erni

## Slide 6: What is ROS?

## Slide 7: What is ROS?
The Robot Operating System (ROS) is a flexible framework for writing robot software. It is a set of software libraries and tools that help to simplify the task of creating complex and robust robot applications. It provides:
  Hardware abstraction
  Low level device control
  Message-passing between processes
  Programming language independence
  Implementation of a wide range of commonly used tools and algorithms
  Package management
Swiss Software Engineering: betterask.erni

## Slide 8: ROS philosophy
Peer to Peer. Individual programs communicate over defined API (ROS messages, services, etc.).
Distributed. Programs can be run on multiple computers and communicate over the network.
Tools based. ROS is based on a microkernel design which uses a large number of small tools to build and run various ROS components.
Multi-lingual. ROS modules can be written in any language for which a client library exists (C++, phyton, java, MATLAB, etc.).
Light-weight. Stand-alone libraries are wrapped around with a thin ROS layer.
Hardware agnostic
Free and open-source. Most ROS software is open-source and free to use
Swiss Software Engineering: betterask.erni

## Slide 9
ROS architecture

## Slide 10: ROS architecture
ROS architecture can be described at three different levels:
  Computation graph level: covers the peer-to-peer network of ROS processes, roles and communications.
  Filesystem level: describes how ROS is organized and configured
  Community level: describes the resources available to exchange software and knowledge across different communities.
Swiss Software Engineering: betterask.erni

## Slide 11: ROS computation graph level
Swiss Software Engineering: betterask.erni

## Slide 12: ROS computation graph level - Concepts
Nodes: Nodes are processes that performs computation. Typical examples are sensor drivers, actuator drivers, high level algorithms, user interfaces, etc. A robot system usually comprises many nodes.
Messages: A data structure used to communicate between nodes.
Topics: A node sends out a message by publishing it to a given topic. The topic is a name that is used to identify the content of the message.
Swiss Software Engineering: betterask.erni

## Slide 13: ROS computation graph level – The Master
Master: Provides name registration and lookup to the rest of the computation graph. Without the master, nodes would not be able to find each other, exchange messages or invoke services.
Swiss Software Engineering: betterask.erni

## Slide 14: ROS computation graph level – Services
Services: The publish/subscribe model is a very flexible communication paradigm but it is not appropriate for request/reply interactions (which are often required in a distributed system). Request/reply is done via services.
Swiss Software Engineering: betterask.erni

## Slide 15: ROS computation graph level – Concepts
Swiss Software Engineering: betterask.erni
Bags: A format for saving and playing back ROS message data. Bags are an important mechanism for storing data, such as sensor data, that can be difficult to collect but is necessary for developing and testing algorithms.
Parameter server: Allows data to be stored by key in a central location. It is currently part of the Master. It is used for static data such as configuration parameters. Parameters can be defined in .yaml files.

## Slide 16: ROS filesystem level
Swiss Software Engineering: betterask.erni
A collection of packages which share a common VCS system
Special packages which only serve to represent a group of packages
Main unit for organizing code in ROS. It contains runtime processes, ROS-dependent libraries, configuration files, etc. The most granular thing you can build and release is a package
Message description. Define the data structures for ROS messages
Service description. Define the request and response data structures for ROS services
Package metadata, including its name, version, description, license, dependencies, etc.

## Slide 17: ROS filesystem level – Package structure
Swiss Software Engineering: betterask.erni
Package_name
include
src
launch
msg
srv
CMakeLists.txt
package.xml
MANDATORY
OPTIONAL

## Slide 18: ROS filesystem level – Launch files
Swiss Software Engineering: betterask.erni
ROS launch is a tool for launching multiple nodes. Are written in XML as *.launch files. If not yet running, ROS launch automatically starts the master.
There are multiple tag options:
  <include> enables you to import another xml file into the current file.
  <remap> For remapping topic names.
  <param> defines a parameter to be set on the parameter server.
  <arg> useful to create reusable launch files by specifying values that are passed via the command-line, an <include> tag or declared for high-level files.

## Slide 19: ROS Community level
Swiss Software Engineering: betterask.erni
Distributions. ROS distributions are collection of versioned stacks that you can install.
Repositories. ROS relies on a federated network of code repositories.
The ROS wiki. http://wiki.ros.org/Documentation main forum for documenting information about ROS.
Bug Ticket System. http://wiki.ros.org/Tickets
Mailing Lists. http://wiki.ros.org/Support primary communication channel about new updates.
ROS answers. https://answers.ros.org/questions/
Blog. http://www.ros.org/news/

## Slide 20
ROS Tools and Commands

## Slide 21: ROS Commands (I)
Swiss Software Engineering: betterask.erni
Filesystem management commands
$ catkin_create_pkg <package_name> [depend1] [depend2]
Creates a new ROS package
$ catkin_make
Builds a ROS catkin workspace
$ roscd <package_name>
Change directory to a package
Start-up commands
$ roscore
The basis nodes for ROS-based systems
$ rosrun <package_name> <node_name>
Runs a ROS package’s executable
$ roslaunch <package_name> <launch_file_name>
Starts a roscore (if needed), multiple nodes and set parameter server parameters

## Slide 22: ROS Commands (II)
Swiss Software Engineering: betterask.erni
Introspection commands
$ rosnode
Displays debugging information about ROS nodes
$ rostopic
Displays information about ROS topics
Options:
  : Lists active nodes
  : Prints information about an active node
  : Kills an active node
Options:
  : Lists all published topics
  : Prints information about an active topic
  : Displays publishing rate of topic
  : Prints messages to screen

## Slide 23: ROS Commands (III)
Swiss Software Engineering: betterask.erni
Logging commands
$ rosbag
A set of tools for recording and playing back ROS topics
Options:
  : Records a bag file with specified topics.
  : Plays content of one or more bag files.
  Summarizes the content of a bag file.
https://github.com/ros/cheatsheet/releases/download/0.0.1/ROScheatsheet_catkin.pdf
Almost all ROS commands and tools in a single document:
Wiki for all ROS commands and tools:
http://wiki.ros.org/ROS/CommandLineTools

## Slide 24: ROS Tools - rqt_graph
Swiss Software Engineering: betterask.erni
rqt_graph provides a GUI plugin for visualizing the ROS computation graph.

## Slide 25: ROS Tools - rqt_bag
Swiss Software Engineering: betterask.erni
rqt_bag provides a GUI plugin for displaying and replaying ROS bag files.

## Slide 26: ROS Tools - RVIZ
Swiss Software Engineering: betterask.erni
3D visualization tool for ROS